## Slide 1
Interrupt controller unit (ICU)
  Self - investigation
Date:
Name: Phuc Che
engineer, RA fsp1,
fsp1
Renesas Electronics Corporation

## Slide 2: Agenda
Overview Page 03
ICU operation Page 06
FSP of ICU Page 11
Appendix Page 17

## Slide 3: overview what is ICU ?
ICU is the short term of Interrupt Controller Unit
As his name, he has responsibility of management the event signal which are linked to Nested Vector Interrupt Controller (NVIC), the DMA Controller (DMAC)and the Data Transfer Controller (DTC)
Moreover, he also controls the non-maskable interrupts

## Slide 4: overview what is ICU ?
Note: This diagram took from HWUM of RA4M3
ICU perform below operation:
+ Detecting interrupts
+ Enabling and disabling interrupts
+ Selecting interrupt request destinations such as CPU interrupt, DTC activation, or DMAC activation

## Slide 5: overview what is ICU ?
There are 2 types of interrupt which handled by ICU:
+ Maskable interrupt
+ Non-maskable interrupt
Able to be disabled or ignored by MCU
Unable to be disabled or ignored by MCU
Note: There may be some others type of interrupt depend on the classification
Typically, the Maskable is interrupt which come from the external interrupt, peripheral, DMAC, DTC, …
The Non-Maskable is interrupt which will handle for HW error, high priority jobs …

## Slide 6: ICU operation how he works – interrupt Vector table
What is “Vector table” ?
Note: Above table took from RA4M3HWUM
In the memory of ARM, there is an area of memory which will be reserved for storing the address of interrupt/exception routine
In short, the Vector table is the table of memory, at each address, the address of ISR/exception which handle for the interrupt will be stored.
An example about vector table which generated by e2studio
The start address of Vector table is 0x00000000
Address of IRQ25 is 0x000000A4
25 is the order of IRQ in the vector table

## Slide 7: ICU operation how he works – eVent table
Note: Above table took from RA4M3HWUM
What is “Event table” ?
The “Event table” used to indicate the event number, interrupt name, connectivity of all interrupts supported by RA chip.

## Slide 8: ICU operation how he works – why vector table/event table matter ?
The event number of IRQ being configured
The “n” based on the order of IRQ in the vector table
Example configuration for IRQ10
Event number is needed to setup the register for telling the MCU where the interrupt event come from.
For the vector table, the address of ISR will be assigned to special area of MCU memory.
When IRQ occur, signal will be identified from which module, after that he will be sent to NVIC, NVIC will call the ISR function by access the address assigned to interrupt vector table.

## Slide 9: ICU operation how he works – interrupt source
Non-maskable interrupts signal source
External interrupts signal
Interrupts signal of peripheral
Signal from DMAC/DTC
When an event occur in the execution of MCU, signal will be sent to ICU
ICU will classify the signal depend on his event number and send to specific HW

## Slide 10: ICU operation how he works – interrupt source
External interrupts, peripheral interrupts, non-maskable interrupt will be sent to NVIC for CPU executing their ISR
Signal of DTC will trigger the IRQ to DTC module
Signal of DMA will trigger the IRQ of DMAC module

## Slide 11: FSP OF ICU API
R_ICU_ExternalIrqOpen(): Configure an IRQ input pin for use with the external interrupt interface
R_ICU_ExternalIrqEnable(): Enable external interrupt for specified channel at NVIC
R_ICU_ExternalIrqDisable(): Disable external interrupt for specified channel at NVIC
R_ICU_ExternalIrqCallbackSet(): Updates the user callback and has option of providing memory for callback structure
R_ICU_ExternalIrqClose(): Close the external interrupt channel

## Slide 12: FSP OF ICU config with e2studio

## Slide 13: FSP OF ICU config with e2studio
Interrupt channel which being configuring
The trigger edge of interrupt
Note: the interrupt signal is active low
Digital Filtering will remove signal which has width less than 3 sampling cycles
Only valid when Digital Filtering was enabled
User callback function for interrupt
Priority of the interrupt
Selected interrupt channel and his corresponding pin port
Note: This configuration is used for external interrupt operation only

## Slide 14: FSP OF ICU config with e2studio
Note: This configuration is used for external interrupt operation only
When added ICU stack, r_icu_isr() will be generated by default and user cannot change it
User can add the ISR as their desire
Callback function will be invoked by r_icu_isr()

## Slide 15: FSP OF ICU config with e2studio
Note: This configuration is used for external interrupt operation only
How to add user’s interrupt event

## Slide 16: FSP OF ICU example – USING API
hal_entry() when using ICU via API
Callback function for ISR
The example will control green LED and blue LED via switch S2 on EK-RA4M3.
Each time pressing the SW, LED will be turned on and off when release, and after 3 times the color will change
Note 1: Example was stored at S:\20_user\phucche\FSP\00_Investigation\RA4M3_ICU_trial
Note 2: Board used for the example is EK-RA4M3

## Slide 17: FSP OF ICU example – USING REGISTER
hal_entry() when using ICU via API
The example will control red LED via SW S1.
When pressing, LED will be turned on and turned off when release
Note 1: Example was stored at S:\20_user\phucche\FSP\00_Investigation\RA4M3_ICU_trial
ISR to control the LED
Note 2: Board used for the example is EK-RA4M3

## Slide 18: Q&A

## Slide 19: appendix reference material
Interrupt classification: https://www.geeksforgeeks.org/interrupts-8085-microprocessor/
Vector table: https://microcontrollerslab.com/what-is-interrupt-vector-table/
NVIC: The Definitive Guide to ARM Cortex -M0 and Cortex-M0+ Processors.pdf

## Slide 20: appendix abbreviation
NVIC: Nest Vector Interrupt Controller
DMA: Direct Memory Access
DMAC: Direct Memory Access Controller
ISR: Interrupt service routine
IRQ: Interrupt request
CPSCU: CPU System Security Control Unit

## Slide 21
Renesas.com